## Slide 1
GDB
PARCELS <<FC>>
Count Rows
int(arcpy.GetCount_management(“PARCELS”)[0])
IF
SINGLE
Count = 1
Count > 1
FAIL
Count = 0
Polygon Neighbor Analysis
arcpy.PolygonNeighbors_analysis(“PARCELS”, “NEIGHBORS”, “OBJECTID; Shape_Area”, “AREA_OVERLAP”, “BOTH_SIDES”, None, “FEET”, “SQUARE_FEET”)
NEIGHBORS <<TBL>>
Count Rows
int(arcpy.GetCount_management(“NEIGHBORS”)[0])
IF
SEPARATE
Count = 0
Count > 0
Dual Looping Structure
with arcpy.da.SearchCursor(“PARCELS”, ...) as cursor1: for row1 in cursor1:
poid = row1[0] (...)
with arcpy.da.SearchCursor(“NEIGHBORS”, …) as cursor2:
for row2 in cursor2:
src, nbr, area = row2[...] (...)
NBRSUM <<TBL>>
Summary Attributes
arcpy.gapro.SummaryAttributes(“NEIGHBORS”, “NBRSUM”, “src_OBJECTID”, “src_OBJECTID SUM”)
Table Query | 
POID | Parcel ID (OBJECTID from PARCELS FC)
SRC | Parcel source ID from NEIGHBORS TBL
NBR | Parcel neighbor ID from NEIGHBORS TBL
AREA | Areas in sq. feet (for SRC-NBR)
SUM | Count parcels from NBRSUM TBL
IF
POID Not in SRC
IF
POID n SRC
Overlap > 0
IF
Overlap = 0
NOT A PART
MAIN PARCEL
SUM = 1
SUM > 1
if SUM = N-1, then single main parcel
PARCEL TYPE
Geodatabase
Feature Class/Table
Python Operation
Decision Node
Output Process Node
Terminal Node
Parcel Detection Algorithm Flowchart AMC Python Script, version 1.6
Dr. Kostas Alexandridis | OC Survey Geospatial Services
add/modify FC field
END